From the Ministry of Environment and Forestry:

# REGULATION ON CONTROL OF WASTE OILS

CHAPTER 1

Objective, Scope, Legal Basis, Definitions, Principles

## Objective

Article 1 – This regulation herein provides for the rules to

- prevent direct or indirect release of waste oils to the receptor medium,

- ensure temporary storage, handling and disposal thereof without causing harmful effects on the environment and human health,

- set up technical and administrative standards for management of waste oils,

- install temporary storage and recovery facilities, and to define the legal bases on related principles, policies and programs for environmental-friendly management of such facilities.

## Scope

Article 2 – This Regulation sets forth prohibitions, limitations and liabilities, measures to be taken, controls to be made as well as legal and penal responsibilities to be followed for generation, temporary storage, collection, handling, recovery, disposal, trade, exportation, importation and transit passage of Category I, II and III waste oils listed in ANNEX I.

## Legal Basis

Article 3 – This Regulation has been issued on the legal basis provided for in Articles 8, 11 and 12 of the Law on Environment no 2872 published in the Official Gazette of August 11, 1983 no 18132 and Articles 1 and 2 of the Law on Establishment and Duties of the Ministry of Environment and Forestry no 4856 published in the Official Gazette of May 08, 2003 no 25102 in accordance with the objectives and principles referred to in Articles 1 and 3 of the Law on Environment, as well as the objectives and principles of as per paragraphs (d), (h), (o), (p) and (s) of Article 9 thereof.

## Definitions

Article 4 – In this Regulation, the terms listed below shall have the meanings given next to them.

The Ministry: The Ministry of Environment and Forestry

Regulation: Regulation on Control of Waste Oils,

Regulation on Control of Hazardous Wastes: Regulation on Control of Hazardous Wastes published in the Official Gazette of August 27, 1995 no 22387,

Oil: Lubrication products of mineral/synthetic base and/or containing necessary additives, supplied to the market for the use they are originally intended,

Base Oil: Petroleum product or synthetically (chemically) produced oil of aliphatic, aromatic and mixed (aliphatic + aromatic) base produced in the refinery,

Waste Oil: Used vehicle oils (oils used in gasoline engine, diesel engine, gearbox and differential gear, transmission, two-cycle engine, hydraulic brake, antifreeze, grease and other special vehicle lubricants), industrial oils (oils for hydraulic systems, turbines and compressors, sliding gears, open-closed gears, circulation, metal cutting and working, metal ductile, textile, heat treatment, heat transfer, isolation and protector, rust and corrosion, isolation, transformers, molds, steam rollers, pneumatic system protector, food and pharmaceutical industry, general purpose, paper machines, beds and other special purpose industrial oils and greases), special preparates (thickeners, protectors, cleaners and other) and contaminated oil products,

Category I Waste Oil: Waste oils listed in ANNEX I permitted for recovery and suitable for recovery by means of regeneration and refining,

Category II Waste Oil: Waste oils listed in ANNEX I that can be recovered as additional fuel in facilities licensed by the Ministry,

Category III Waste Oil: Waste oils listed in ANNEX I, not suitable for refining, causing risks for human health and environment when used as additive fuel and that must be disposed at hazardous waste disposal facilities,

Waste Motor Oil: Waste oils originating from motor vehicles at the end of a certain period of use, but not suitable for the use they are originally intended,

Oil Producer: Real and legal entities producing (other than refinery) and/or importing oil for the use originally intended or operating the facilities that have the capacity to transform waste oils into base oil or petroleum products in accordance with national and international standards,

Waste Oil Generator: Real and legal entities causing formation of waste oils listed in ANNEX I during their activities or holding such waste oils when the originator is unknown,

Waste Motor Oil Generator: Real and legal entities, institutions or agencies generating waste motor oils or holding such waste oils when the originator is unknown,

Disposal: Recovery or discarding of waste oils at the facilities licensed by the Ministry or combustion thereof at licensed combustion facilities,

Combustion: Disposal of waste oils at licensed hazardous waste combustion facilities in accordance with the provisions of the Regulation on Control of Hazardous Wastes,

Recovery of Waste Oils: Regeneration, refining and power-related use of waste oils as additives at licensed facilities,

Regeneration: Removal of all pollutants, oxidation products and particles from the waste oil to result in original oil suitable for the use intended as per national and international standards and specifications,

Refining: Transformation of waste oils into base oil or petroleum products after being refined in accordance with national and international standards,

Temporary Storage: Holding of waste oils by the generators within the field of activity for a certain period of time or provisional storage of waste oils by the producers of oil and generators of waste oil for collection purposes at the retail sales and/or oil change spots,

Collection of Waste Oils: All actions taken by the waste oil generator from classification to disposal for handling by licensed transporters with National Waste Transportation Form,

National Waste Transportation Form: Forms given in ANNEX 9B of the Regulation on Control of Hazardous Wastes,

Waste Oil Declaration Form: Form given in ANNEX 2,

Prelicense: The certificate issued for those willing to establish and operate facilities to recover waste oils under the scope of this Regulation confirming compliance of projects to the requirements of environment and human health,

License: The certificate issued by the Governor’s Office for transportation companies willing to transport waste oil under this Regulation and by the Ministry for those willing to establish and operate waste recovery facilities confirming that they have sufficient capacity and technology,

Quota: Proportion of waste motor oils that need to be recollected and disposed to the amount of oil put in the market,

Enterprises Subject to Quota Application: Motor oil producers, those putting motor oil in the market under their own brand, and importers thereof,

Quota License Application Form: The form given in ANNEX 3,

PCB: Polychlorinated Biphenyls,

PCT: Polychlorinated Terphenyls.

### General Principles

Article 5 – The principles to be followed for management of waste oils are as follows:

- It is prohibited to discharge waste oils including waste motor oils and residues resulting from processing of waste oils to open grounds or to replace or to store them or to deposit them into internal surface waters, ground waters, coastal waters, drainage systems and to soil, and to process waste oils causing air pollution which exceeds the level prescribed by existing provisions.

- Waste oils shall not be mixed with water, solvents, PCB/PCT, toxic and hazardous substances and other substances as well as other waste oils in different categories. Waste oils shall be temporarily stored, handled and disposed in separate tanks/containers according to the categories referred to in ANNEX I. Result of the mixture of category I oil with category II oil shall be accepted as category II waste oil, whereas category I and II oils with category III oil as category III waste oil.

- Waste oil formation shall be minimized at source; and when generation is inevitable regeneration and refining of waste oil shall be the first option for recovery. Waste oils that do not meet the required level of quality for base oil and petroleum product by the end of recovery procedures of category I and II waste oils and category I oils shall be available for use as additional fuel at the facilities licensed by the Ministry and listed in Article 22. Waste oils that cannot be recovered shall be disposed as described in Article 23 at the waste disposal facilities licensed by the Ministry.

- Waste oil generators, transporters, recoverers and disposers shall be held liable for any environmental pollution and degradation due to waste oils notwithstanding their failure. In any damage resulting from such activities, the indemnity liability of generators and marketing authorities shall be proportional to their failure.

- Provisions of the Regulation on Control of Hazardous Wastes shall apply in international trading, importation, exportation and transit passage of waste oils under the scope of this regulation.

- Financing of indemnities arising from any damage to the environment due to mismanagement of waste oils shall be made by real and legal entities responsible for management of wastes in accordance with the “polluter pays” principle. Expenditures by public authorities and agencies due to lack of action by those responsible for management of waste oils made to stop, compensate for and reduce environmental degradation or due to measures taken directly by related authorities shall be collected from those responsible for management of waste oils as per the Law on Collection of Public Claims no 6183.

- It is prohibited for real and legal entities other than those licensed by the Ministry to collect, purchase, sell and dispose waste oils or to combust such oils by mixing with fuel oil or other liquid fuels.

#### CHAPTER 2

Duties, Authorities and Liabilities

Duties and Authorities of the Ministry

Article 6 – The Ministry shall be entitled and authorized to

- define policies and programs ensuring environmental-friendly management of waste oils, create a medium of cooperation and coordination for implementation of this Regulation,

- issue pre-licenses and licenses to recovery facilities and undertakings that intend to use waste oils as additional fuel,

- set quotas for collection and recovery of waste motor oils for coming years as defined in Article 12 of the Regulation for the first five years, ensure their application,

- ensure national and international coordination to implement the state-of-the-art systems and technologies for environmental-friendly management of wastes.

## Duties and Authorities of the Senior Public Officer

Article 7 – The senior public officer shall be entitled and authorized to

- identify and notify to the Ministry the existing and planned waste oil generating facilities, recovery and combustion facilities that are active under his/her jurisdiction and that fall in the scope of this Regulation,

- regularly audit waste oil handlers and recovery facilities in terms of their compliance with the licensing conditions, to carry out the necessary administrative proceedings and to notify the Ministry of the results of such proceedings,

- prevent use of waste oils for purposes other than those defined in this Regulation, such as direct heating, power generation, construction sector, industry, motor vehicles and other similar illegal means of use, to ensure transport of any illegally used waste oil to the closest disposal facilities and to fine the related parties as defined in this Regulation,

- collect waste oil declaration forms (ANNEX 2) filled in by waste oil generators, to make them cover the gaps, if any, and to send the forms to the Ministry at the end of each year,

- evaluate the annual reports and National Waste Transportation Forms to be provided by the recovery facilities, and to notify the Ministry of the amount of waste oil accepted to the facilities according to waste oil categories, the products obtained and amount thereof, fields of use, the amount of wastes not recovered at those facilities and how they are disposed,

- license the vehicles and companies registered in his/her jurisdiction to undertake transportation of waste oils, to inspect their activities, to notify the Ministry of the vehicles and companies so licensed,

- take all kinds of contingency measures and make necessary coordination against all possible accidents that may take place during transportation of waste oils within the provincial borders,

- issue construction licenses to the waste oil recovery facilities to be established outside the municipal and peripheral borders.

##### Duties and Authorities of the Municipalities

Article 8 – The Municipalities shall be entitled and authorized to

- reject waste oils at the domestic solid waste storage fields,

- prevent waste oils from being dumped into the sewer system or directly deposited to receptor media such as water or soil,

- issue construction licenses to the waste oil recovery facilities to be established outside the municipal and peripheral borders.

##### Liabilities of Waste Oil Generators

Article 9 – Waste oil generators shall be liable to

- take measures to minimize waste oil generation,

- analyze / have analyzed the waste oils according to the parameters laid down in ANNEX 1 and to identify categorization of waste oils so analyzed, to temporarily store, handle or have handled waste oils separately according to their categories,

- avoid mixture of waste oils from different categories or with PCB, PCT and other hazardous wastes, to abide by the provisions of the Regulation on Control of Hazardous Wastes for oils contaminated with hazardous wastes,

- establish or have established recovery or disposal facilities, to have pre-licenses and licenses taken from the Ministry for such purposes, to make use of the existing facilities,

- have waste oils transported to licensed disposal facilities by licensed handlers and to have them disposed there,

- fill in the National Waste Transportation Form when and where waste oils are transported outside the facilities,

- keep in their facilities waste oil declaration forms, analysis certificates, papers confirming amount of waste oil, national waste transportation forms, invoices, dispatch notes, weighing scale receipts and other documents to be asked by the Ministry for 5 years for submission to authorities during an inspection or whenever requested,

- temporarily store waste oils as described in Article 19 of this Regulation herein,

- fill in the waste oil declaration forms (ANNEX 2) for the previous year and provide them to the governor’s office by the end of February next year (this provision excludes waste motor oil generators),

- bear necessary expenses to categorize waste oils,

- notify the governor’s office and the Ministry within 15 days of any and all disputes between the generator and the disposal undertaking regarding transportation of waste oils, had such disputes not be overcome within this time span, and to store such disputable waste oils in their own facilities throughout this period.

## Liabilities of Motor Oil Producers and Importers

Article 10 – Motor oil producers and importers shall be liable to

- ensure recollection, disposal or exportation of waste motor oils emerging after use within the quotas laid down in this Regulation, to make related declarations to the Ministry, and to pay necessary charges for proper management of such wastes as per the Regulation,

- set up or have set up the necessary systems for collection of waste motor oils, to provide suitable temporary storage houses, to establish or have established recovery or disposal facilities, to get pre-license and license from the Ministry for this purpose, and to make use of the existing facilities,

- get permits from the Ministry for quota application to waste oils emerging from use of motor oils within the framework of the principles laid down in Articles 12, 13 and 14 of this Regulation, to fill in the form given in ANNEX 3 covering the amount of oil produced annually, and to make declaration to the Ministry by the end of January every year,

- provide and display warnings and symbols on the labels of the motor oils available at the market, at the sales point of such products and in temporary storage points as described in ANNEX 4 A, B and C relating to the procedure for collection, temporary storage, recovery and/or final disposal of waste oils,

- carry out the necessary works for raising awareness and educating the public on recollection and management of waste motor oils in accordance with this Regulation herein,

- prepare reports at the end of every year on waste oil collection, handling, recovery and disposal activities as well as the existing situation, problems encountered, investments planned and made, collection and recovery targets, and to submit such reports to the Ministry.

## Liabilities of Waste Oil Recovery Undertakings

Article 11 – Waste oil recovery undertakings shall be liable to

- build their facilities in accordance with the principles laid down in this Regulation, to get pre-license from the Ministry at the project design phase and to be licensed to operate the facilities built as per the project,

- abide by the conditions stipulated by the Ministry in case the Ministry demands change in plans or issues conditional license,

- send annual reports to the governor’s office about their activities,

- define acceptance criteria for waste oils, check whether the waste oil matches the definition provided in the waste oil transportation form, and when the waste oil is to be transformed into base oil or petroleum product after recovery, to get approval and certification from the Directorate General for Petroleum Works, Ministry of Energy and Natural Resources for quality of the product as per Article 27,

- get samples taken from recovered products and to have such samples delivered to the laboratory by the technical staff of the institutions/agencies in charge of market surveillance and supervision of such products or of the Provincial directorate of Industry and Trade to be analyzed in accordance with the standards of the Turkish Standards Institute,

- analyze waste oils received at the facilities, to check their compliance with the generator’s declaration, to sign and receive the National Waste Transportation Form when deemed appropriate, and to send such forms to the governor’s office within one month,

- avoid mixture of waste oils with PCB, PCT and other hazardous wastes, to store them separately according to their categories, to categorize oils contaminated with hazardous wastes as category III oils and to follow the provisions of the Regulation on Control of Hazardous Wastes for such oils,

- train the personnel, to prepare contingency plans, to take records on waste management and to keep such records at the facilities for five years,

- ensure safety of the personnel working in risky sections of the facilities, to prevent unauthorized access to such sections,

- keep trained personnel on contingency measures, to notify any contingency to the Ministry and the governor’s office,

- dispose the wastes emerging from recovery works and contaminated packages in accordance with the provisions of the Regulation on Control of Hazardous Wastes,

- reject waste oils coming from handlers without transportation form and license and to inform the governor’s office about the situation,

- operate the facilities as required by the Ministry and in line with the license conditions.

CHAPTER THREE

Quota Application on Waste Motor Oil

# Application of Quota on Waste Motor Oil and Liabilities

Article 12 – The Ministry requires quota application with regards the collection and recovery or disposal by combustion or exportation of waste motor oil so as to ensure environment friendly management of waste motor oil and to prevent degradation of ecological balance.

Motor oil producers, those releasing motor oil products to the market under their own brand and those importing the same shall be liable to collect/have collected, recover or dispose of waste motor oils in the ratio of 8% over the production quantity realized as from the date of enforcement of this Regulation until the end of the year for the first year, 12% for the second year, 20% for the third year, 25% for the fourth year, 30% for the fifth year and in the ratios to be identified by the Ministry for the subsequent years and shall be liable to document such procedures before the Ministry. The undertakings to this end shall be liable to receive a license from the Ministry and to submit a declaration to the Ministry.

Motor oil producers, those contracting out the production or those selling import motor oils in the market may gather to establish a non-profit legal entity under the coordination of the Ministry so as to minimize the impact of such products to the receptor media, to fulfill the liabilities arising from the collection, handling, recovery and disposal of waste motor oils, to cover the relevant expenditures and to perform training activities. The organizations fulfilling their liabilities before this entity and contributing to the expenditures may delegate their collection and recovery liabilities to this entity. Those involved in such an entity shall be responsible for meeting the quota requirements.

In case of failure to meet quota requirements, penalties stipulated under articles 15, 20 and 21 of the Law on Environment No. 2872 shall apply for the motor oil producers, those releasing motor oil products to the market under their own brand and those importing the same.

Permit Application for Waste Motor Oil Quotas

Article 13 - Motor oil producers, those releasing motor oil products to the market under their own brand and those importing the same shall apply each year to the Ministry for quota permit until the end of the last work day of the month January by filling the “Quota Permit Application Form” given in ANNEX 3. The undertakings shall declare in this form the type, production and sales quantities of the motor oil filled, imported and sold in the market; information on temporary storage, collection, handling, recovery and/or combustion or exportation of waste motor oil and shall submit the related documents. The Ministry may require additional information and documents, if necessary.

Assessment of the Permit Application

Article 14 – In case the Ministry finds the information and documents specified under article 13 sufficient, the Ministry shall grant a permit to the relevant motor oil producer for quota application on waste motor oils. Validity of the permit is maximum one calendar year. The same quota rate shall apply for applications made during times other than the regular permit application. In case the requirements of this Regulation are not met and the information provided under article 13 are found to be inaccurate, a penalty shall apply to the producer company as per the Law on Environment No. 2872 and the provisions of this Regulation. Furthermore, the Ministry may have the declarations made under article 13 of this Regulation for permit application audited by sworn financial consultants. Expenditures thereof shall be borne by the relevant companies.

Exported motor oils, marine motor oils, two-cycle motor oils added to fuel and biodegradable oils are excluded from quota application. However, such undertakings shall fill in the Quota Permit Application Form given in ANNEX 3 and submit a declaration to the Ministry.

Informing the Consumer

# Article 15 - Motor oil producers, those releasing motor oil products to the market under their own brand and those importing the same shall be liable to place the warnings and information specified in ANNEX 4/A and the symbol given in ANNEX 4/C at the sales points of motor oil products, temporary storage facilities and the other relevant locations; the warnings and information specified in ANNEX 4/B and the recoverable waste oil symbol specified in ANNEX 4/C on the labels of the motor oil packages, in a manner to be visible to and eligible for the consumers and users. This symbol is characterized by a yellow oil drop and three green circular arrows following each other inside this drop. The symbol shall be placed on the description side of the product label and shall be in the size of at least 20% of the company logo used or not less than 0.5 cm2.

## CHAPTER FOUR

Provisions on Transportation

# Waste Oil Transportation

Article 16 – Transportation of waste oils shall be performed with the means appropriate to the waste oil category by the real and legal persons licensed for transportation from the relevant governor’s office. Same category of waste oil shall be transported in the same vehicle and same container. The transporter shall have vehicles separately dedicated for waste oil categories I, II, III or shall have the appropriate technical means for the handling of waste oils of different categories in the same vehicle without mixing up with each other. Outer surface of the waste oil transportation vehicle shall be red and the wording “Waste Oil Transportation Vehicle” shall be inscribed on the tank and the category of the waste oil transported shall also be specified. Products other than the specified ones shall not be placed in and transported with these vehicles.

Requirement for the Availability of Waste Transportation Form in the Vehicles

Article 17 – It shall be required to have waste transportation form available in the vehicles during transportation of waste oils. Relevant provisions of the Regulation on Control of Hazardous Wastes shall apply with regards the waste transportation forms to be available in the vehicles.

Licensing Requirement for Waste Oil Transporters

Article 18 – Real and legal persons to transport waste oil shall be liable to have a license for waste oil transportation. They shall apply to the relevant governor’s office as per the bases specified in ANNEX 5. License shall be granted to the company owning the applicant vehicle/(s) and the vehicle/(s) bearing the required technical means. These provisions shall apply for land transportation. The license shall by no means be transferred and shall be valid for 3 years. The license shall be renewed at the end of this period. The licenses of the companies, which are already licensed by the governor’s offices however are failing to comply with the proposed standards in transportation shall be cancelled.

## CHAPTER FIVE

Temporary Storage, Recovery Facilities and Disposal of Waste Oils

# Temporary Storage

Article 19 – Waste oils shall be collected inside the tanks/containers placed on an impermeable surface, details of which are given under paragraph (g), article 21. Different tanks/containers shall be used for waste oils of different categories. Waste oil temporary storage tanks/containers shall bear displays, shall have a mechanism against overloading and shall be filled until the marked level. Waste oil temporary storage tanks/containers shall by no means be left as filled up to full capacity and shall be easily loaded and discharged. The opening of the tanks/containers shall be in an appropriate size and be enclosed. The tanks/containers shall have the necessary mechanism to allow for the cleaning of the solid or sludge-like deposits from the bottom of the tanks/containers and shall be protected against storm water.

Tanks/containers shall be red and shall bear “Waste Oil” wording. Waste oils of different categories shall by no means be mixed with each other. Any foreign matter such as water, gasoline, fuel-oil, paint, detergent, solvent, antifreeze and diesel-oil shall not be added onto the content of these tanks.

Temporary Storage Tanks/Containers for Motor Oils

# Article 20 – Motor oil producers shall construct waste motor oil temporary storage facilities at the locations close to the sales points, at vehicle maintenance, inspection and service stations, gas stations and the similar locations so as to collect waste motor oils. Warnings and information specified under ANNEX 4/A and the symbol given under ANNEX 4/C shall be placed in a manner to be visible to, eligible for and accessible by the consumers and users. Article 20 of the Law on Environment No. 2872 shall apply for the temporary storage undertakings performing sales activities or using the facilities in a manner contradicting with the provisions of this Regulation.

Volume of waste motor oil temporary storage tanks/containers shall be minimum 200 lt. and maximum 1250 lt. and shall be protected against storm water. Tanks/containers shall be red and shall bear the wording “Waste Oil”. Oil filters removed from the vehicles shall be kept inside a separate enclosed container located next to the waste motor oil temporary storage tanks. They shall by no means discarded in the waste bin or sent to the garbage dump area. “Oil Filter” wording shall be inscribed on the used oil filter container and be protected against storm water. These filters, after being unloaded, shall be disposed of as per the Regulation on Control of Hazardous Wastes.

Waste oil temporary storage tank and oil filter containers shall by no means be used by operators not bearing the required technical capability. The surface on which the tanks and containers are placed shall be impermeable and the location shall be enclosed so as to prevent unauthorized access and the necessary measures shall be taken against potential spills and fires.

Special Provisions for Waste Oil Recovery Facilities

Article 21 – The following provisions shall be abided by in the waste oil recovery facilities:

- Only category I waste oils shall be recovered at the waste oil recovery facilities through refining and regeneration.

- Reception area, incoming waste unit, storage area, laboratory, process unit and other work units shall be present at the facilities.

- The facility shall allow for the entry and exit of waste oil transportation vehicles or for the unloading of oil in the tanks.

- The facility shall be enclosed for protection, a fence or a wall shall be constructed for controlled entry and exit and access of people other than the authorized personnel shall be prohibited.

- Tanks or containers used at the facility shall have a display and measures shall be taken against overloading. Tanks or containers shall by no means be left as filled up to full capacity and the tanks/containers shall not be used for any product other than the content of the same. The tanks shall have the mechanism to allow for the cleaning of the solid or sludge-like deposits from the bottom of the tanks, when necessary.

- The licensed vehicle arriving at the facility shall be sent to sample taking unit after being weighed with the waste oil loaded at the incoming unit. The vehicle driver shall take the sample at the sample taking unit under the supervision of the related laboratory personnel. Waste oils as received inside the tank shall be homogenized prior to sample taking. After samples are taken from the waste oils received in barrels, the covers of such barrels shall immediately be closed. Samples shall be kept until the recovery procedures of the relevant waste are completed.

- Surface impermeability shall be ensured for the areas of the facility contacting with waste oil. To this end, reinforced concrete ground having a thickness of at least 25 cm. and the inner surfaces of the retting side walls shall be coated with epoxy paint, geomembrane and similar insulation materials so as to ensure impermeability against spills. Incoming waste area shall be protected against rain.

- Necessary safety measures and measures against spills and leaks shall be taken at the incoming waste oil area.

- Footed tanks shall be preferred for safe and easy response. The tanks shall be red in color, bear the label “Waste Oil” and waste oils of different types shall not be put in the same tank. The tanks shall be placed inside safety pools with a size preventing overflowing. The volume of the safety pool shall be at least at the same capacity with the tank and a safe discharge equipment shall be present. Foam fire extinguisher and water-filled tank cooling systems shall be present near the tanks.

- Pipes carrying waste oil shall be protected against all kinds of leaks and spills. Pipes carrying waste oil shall be located beneath those carrying clean water. Pump pressures shall be designed and adjusted in a manner to avoid any damage to the pipes.

- Storm waters, wash waters and similar waste waters of the area shall be collected separately and be treated in accordance with the limit values specified in the Regulation on Control of Water Pollution.

- Adequate quantity of absorbents shall be made available so as to prevent possible spills and leaks within the facility and shall be stored at locations appropriate for ease of use. Used absorbent materials shall be disposed of as per the Regulation on Control of Hazardous Wastes.

- Noise arising from the working areas shall be minimized to the extent possible in accordance with the criteria given under the Regulation on Noise and Control by using the state-of-the-art techniques.

### Use of Waste Oil as Additional Fuel

Article 22 – Waste oils failing to have the quality for use as base oil or petroleum product as a result of the recovery procedures of category I and II waste oils and category I oils may be used as additional fuel in addition to the existing fuel in the cement plants, gypsum plants, clay plants, clay drying kilns, blast furnaces in iron and steel plants, power plants and waste combustion facilities. Licensing of the Ministry is required for this type of use. Information and documents specified under ANNEX 6 shall be requested for the licensing stage of these facilities. Facilities applying for licensing to combust waste oils are required to perform trial burn. The objective for trial burn is to identify whether the facility meets the emission limit values specified under the Regulation on Protection of Air Quality on the basis of waste menu and waste feed rate. The undertaking shall prepare the trial burn plan and submit it for Ministry approval prior to the trial burn. The trial burn report to be prepared upon the trial burn performed according to the plan approved by the Ministry shall be submitted to the Ministry for consideration.

#### Discarding of Waste Oils through Combustion

Article 23 – Category III waste oils inappropriate for recovery and required to be disposed of in hazardous waste combustion facilities, hazardous type wastes resulting from recovery procedures, contaminated substances thereof and the tank bottom sludge of waste oil storage tanks shall be disposed of in the facilities licensed by the Ministry as per the provisions of the Regulation on Control of Hazardous Wastes.

##### CHAPTER SIX

Provisions on Pre-Licensing and Licensing of Recovery Facilities

and Marketing of Recovered Products

#### Pre-Licensing of Waste Oil Recovery Facilities

Article 24 – Real and legal persons to establish waste oil recovery facilities shall apply to the Ministry by submitting all kinds of plans, projects, reports, technical data, descriptions and similar documents related to the facility to be established. Technical reports as one by the Directorate General of TÜPRAŞ (Turkish Petroleum Refineries Corporation) and one by the related department of a university shall be prepared during the environmental impact assessment studies to be performed for these types of facilities, demonstrating the capability of the technology used in the waste oil recovery facility on the basis of the waste types to be processed in the facilities and the finished products; and the necessary investigation and assessment shall be based on this report.

“Environmental Impact Assessment Positive Certificate” or “Environmental Impact Assessment Not Required Certificate”, EIA Report or EIA Preliminary Study Report and the other information and documents specified in ANNEX 7 shall be submitted for pre-licensing applications. The Ministry shall examine the project on the basis of the above and grant a pre-license to the project in case the ministry finds the project appropriate.

#### Temporary Permit and Licensing for Waste Oil Recovery Facilities

Article 25 – Real and legal persons to establish and/or operate waste oil recovery facilities are liable to receive a license from the Ministry. Facilities complex with units complementing each other and using similar technologies shall be considered as one unit for licensing purposes. Information and documents specified under ANNEX 8 shall be required for licensing of waste oil recovery facilities.

When the waste oil recovery undertaking applies to the Ministry for licensing, a “Temporary Work Permit” shall be granted to the facility to be valid for a period determined by the Ministry so as to document the conformity of the operations with the provisions of this Regulation. The facility, during the period of the permit, shall operate under the supervision of the Ministry. Duration of the permit shall not exceed 1 (one) year. In case the facility fails to meet the operational requirements specified in the pre-license throughout the validity of the temporary work permit, the operations of the facility shall be suspended until the requirements are met.

The Ministry shall grant operational license to the facility provided that the commission, comprising of the authors of the technical report mentioned under article 24 and working under the coordination of the Ministry, identifies on site that the pre-licensed facility has been constructed in conformity with the relevant project and its specification; the operational plan is examined and found to be appropriate; and that the facility meets the operational requirements throughout the validity of the Temporary Work Permit. The license is valid for a period of 3 years and may be granted conditionally when necessary. In case the license is to be transferred, the Ministry shall be applied and the license shall be renewed with administrative approval.

#### Cancellation of the License

Article 26 – In case it is determined as a result of the inspections by the Ministry or the relevant governor’s office that the facility does not operate in conformity with the license, fails to meet the requirements of the legislation, and that the measurements are not regularly performed or recorded, a period varying between one month and one year shall be granted to the undertaking for settling the deficiencies identified, depending on the significance and source of such deficiencies. In case it is identified as a result of the inspection performed by the end of the period granted that the deficiency identified is still not settled, provisions of the articles 15 and 16 of the Law on Environment No. 2872 shall apply, depending on the type of the deficiency identified. In case the facility, operations of which are suspended for a temporary period of time, fails to fulfill its liabilities by the end of this period, its license shall be cancelled. The facility, license of which was cancelled, shall repeat its application before the Ministry as per article 25 for licensing purposes. The facility shall not be operated until the completion of the licensing process.

#### Provisions on Marketing of Recovered Products

Article 27 – It is possible to recover category I oils and to generate products at base oil or petroleum product quality. Base oils can be transformed into quality products by adding certain additives. Recovered oils and all other lubricant oils shall be sold to mineral oil and grease producers or to the companies required to use these oil products as per their capacity reports. Directorate General for Petroleum Works, Ministry of Energy and Natural Resources shall grant a license for use and sales purposes, so as to allow for sales of recovered base oil or other petroleum products in the market.

## CHAPTER SEVEN

Miscellaneous

Breach to the Regulation

Article 28 – Necessary proceedings shall be started against those breaching the provisions of this Regulation by the authorities specified under articles 15 and 16 of the Law on Environment No. 2872 and the penalties specified under articles 20, 21, 22, 23, 24 and 26 of the law in question shall apply.

Authority to Amendment

Article 29 – Unless otherwise stated, the Ministry shall be authorized to make any and all related amendments to this Regulation to facilitate its implementation.

Provisional Article 1 – Waste oil recovery facilities construction and/or operation of which has been started prior to the enforcement of this Regulation and operating without any license from the Ministry and those operating under an operational license shall apply to the Ministry for pre-licensing and/or licensing within 6 months and one year respectively as from the date of enforcement of this Regulation, with the information and documents specified under articles 24, 25 and 26.

Provisional Article 2 – Waste oil generators other than the waste motor oil generators shall fill in the waste oil declaration form and submit the same to the relevant governor’s office by the end of the month February of the year following the date of enforcement of this Regulation.

Enforcement

Article 30 – This Regulation shall be in force as of the date of its publication.

Execution

Article 31 – The provisions of this Regulation shall be executed by the Minister of Environment and Forestry.

ANNEX –1

WASTE OIL CATEGORIES

AND

LIMIT VALUES FOR THE ALLOWABLE POLLUTANT PARAMETERS

CATEGORY 1 WASTE OIL: The pollutants in the waste oils such as PCB, total halogen and heavy metal are below the limit values given in the below table. The waste oils in this category are available for recovery through refining and regeneration or suitable for use as additional fuel in the facilities licensed by the Ministry.

CATEGORY 2 WASTE OIL: The heavy metal content of the waste oils are below the limit values given in the below table. Chloride and total halogens are between the limit values of 200 – 2000 ppm, and PCB is between the limit values 10 – 50 ppm. The waste oils in this category are suitable for use as additional fuel in the facilities licensed by the Ministry.

CATEGORY 3 WASTE OIL: The heavy metal content of the waste oils are above the limit values given in the below table. Chloride and total halogens are above 2000 ppm and PCB is above 50 ppm. The waste oils in this category not only are not available for refining, but also create risks for human health and environment. This category waste oils should be combusted and disposed in the licensed hazardous waste oil combustion facilities.

TABLE

| Pollutants | Allowable Limit Values (Cat. 1 Waste Oils) | Allowable Limit Values (Cat. 2 Waste Oils) | Allowable Limit Values (Cat. 3 Waste Oils) |
| --- | --- | --- | --- |
| Arsenic | < 5 ppm | Maks. 5 ppm | > 5 ppm |
| Cadmium | < 2 ppm | Maks. 2 ppm | > 2 ppm |
| Chromium | < 10 ppm | Maks. 10 ppm | > 10 ppm |
| Chloride | Maks. 200 ppm | Maks. 2000 ppm | > 2000 ppm |
| Lead | < 100 ppm | Maks. 100 ppm | > 100 ppm |
| Total halogens | Maks. 200 ppm | Maks. 2000 ppm | > 2000 ppm |
| Polychlorinated Biphenyls (PCB) 1 | Maks. 10 ppm | Maks. 50 ppm | > 50 ppm |
| Flashing point | Min. 38 C | Min. 38 C | - |

(1) If the Ministry deems appropriate PCB measurements may be made on sector basis.

ANNEX – 2

WASTE OIL DECLARATION FORM OF …………(YEAR)

(To be filled in by the waste oil generators except for waste motor oil generators)

- Name, surname, commercial title, address, telephone and fax numbers, trade registry number and e- mail address of the waste oil generator

- Generation capacity of the facility

- Types, commercial names and amounts (ton/year) of oils used in the facility

a)

b)

c)

d)

- Sources of the waste oil generated in the facility

a)

b)

c)

d)

- Answer the below given questions on waste oils.

  - What is the amount of waste oil in your facility? Specify in tones per year. (Information shall be given separately for the waste oils in different categories)

  - Specify the categories of waste oils (Annex 1)

( Category 1 waste oils

( Category 2 waste oils

( Category 3 waste oils

  - Name of the waste oil used in the facility: .........................

  - Physical state of the waste oil (at room temperature)

(	Fluid		( Sludge		( Jelly 		( Other

- Analysis reports on the waste oils of different categories prepared by official institutions, institutes or universities shall be enclosed herewith.

- Do you store waste oils temporarily in your facility? Briefly explain your storing methods and techniques.

- What are the types and amounts of used oil packages? Specify in pieces / year and tones / year.

( Plastic 		( Metal 	( Paper-cardboard 		( Other

- Do you store used oil packages temporarily in your facility? Briefly explain your storing methods and techniques.

- Which transportation company/companies are you working with for the transportation of the waste oil and used oil packages to the facility / facilities? Specify the address, telephone and fax numbers, name and surname of the responsible personnel of the above.

- Please categorize the waste oils and used oil packages on the basis of generation, recovery /disposal activities and report them according to their amounts (ton/year) and the names and addresses of the recovery/disposal facilities.

# ANNEX – 3

QUOTA PERMIT APPLICATION FORM

1- Information on the Company:

Commercial title of the company:

Code of the Company:

Address:

Telephone number:

Fax number:

E-mail address:

Name and surname of the personnel in charge of environment:

2- Information on production, filling and importation

Types and Amounts of the Oils Produced and Filled in the Facility or Imported to the Facility

(Net sales figures of the previous year shall be taken into consideration)

| Type of the oil | Amount (ton/year) |
| --- | --- |
| 1. |  |
| 2. |  |
| 3. |  |

3- Information on the recovery of the waste motor oils

- What are your plans, projects and arrangements for the collection, recovery and disposal of the waste oils as per the Regulation on Control of Waste Oils?

- Please give commercial title and address information of the undertakings that you have made agreements – if any - for the collection recovery and disposal of the waste oils.

- If the products marketed by your company are imported (Importer company), please enclose the information on the exporter country, commercial title and address of the exporter company, amount and weight of the imported products according to the types of waste oils.

- Please enclose the amount of your waste oil stock herewith.

I hereby certify that the information given in the form is true and authentic and I also acknowledge that I am aware of the penalties to be imposed to the ones issuing false documents as per the Article 26 of the Law on Environment No 2872, provided that the information given in the From is proven to be false. And I kindly request that our quota permit application be accepted as per Articles 13 and 14 of the Regulation on Control of Waste Oils.

Name – Surname- Title and Signature of the Authorities of the Company

## ANNEX – 4/A

The product you have purchased is deemed as waste oil following the expiry period. Therefore following the expiry period products must be handed over to the closest temporary storage facility, recovery or disposal facility so as to protect human health and environment. In this respect; 1. The waste oil shall be placed in a clean, empty, tightly closed, narrow opened, leak proof container to prevent overflow. If possible keep it in its original container. 2. The waste oil shall not be mixed with other fluids such as gasoline, fuel oil, detergent, paint, solvent, anti freeze or diesel oil. The waste oil shall not be disposed of on to soil, water, sewerage system, garbage container and etc and shall not be burned in stove and burners. 3. Oil filter shall be placed in a polyethylene plastic bag which is not perforated and which is resistant to tearing and perforation. 4. Waste oil and oil filter shall not be left idle and shall be kept out of reach of children. Such products shall be handed over to responsible operator of the closest temporary waste oil storage facility, recovery and disposal facility free of charge in 24 hours.

## ANNEX – 4/B

Do not discharge waste oil to soil, water, sewerage system or garbage dumping area. Do not mix waste oil with any petroleum product or chemicals Do not burn waste oil in stoves or burners. Hand over waste oil to the closest waste collection point free of charge in a container, which is clean, sound and tightly closed. Keep out of reach of children.

# ANNEX – 4/C

(symbol)

Recoverable Motor Oil

# ANNEX – 5

INFORMATION AND DOCUMENTATION REQUIRED BY THE GOVERNOR’S OFFICE OF FOR THE LICENSE APPLICATION FOR THE TRANSPORTATION OF WASTE OILS

1. The application file for the licensing of vehicles to be submitted to the Governor’s Office shall include the below mentioned information and documentation.

- Commercial title, address and telephone numbers of the company to which the vehicle belongs.

- Type of the vehicle

- Plate number and chassis number of the vehicle

- Name, surname, business address and telephone numbers of the owner of the vehicle.

- Categories of the waste oils to be transported.

- Type of the waste oil container to be loaded to the vehicle (palleted barrel, tank, etc)

- Physical and chemical properties of the each type of the waste oil to be transported and the measures for minimizing of the adverse effects on human health and environment in case of any accident.

- Materials to be used in the first response and first aid in case of any accident.

- For each vehicle a “Compliance Certificate” issued by the Turkish Standards Institute and showing that the vehicle is equipped with the necessary hardware and properties as per the hazard group of the waste to be transported in accordance with the “Regulation on the Transportation of Hazardous substances on Motorways”.

2- The application file for the licensing of the transportation company to be submitted to the Governor’s Offices shall include the below mentioned information and documentation.

- Commercial title, address and telephone number of the company.

- Name, surname, address and telephone number of the owner(s) of the company.

- Number of the vehicle suitable for waste oil handling.

- Plate numbers of the vehicles to be licensed.

- Driver training certificate issued by the authorized institutions/agencies for the drivers who will transport the hazardous substances.

- Hazardous group number of the waste oils to be transported in accordance with the “Regulation on the Transportation of Hazardous substances on Motorways”.

# ANNEX – 6

INFORMATION AND DOCUMENTATION REQUIRED FOR THE LICENSING APPLICATION FOR THE FACILITIES THAT USE WASTE OILS AS ADDITIONAL FUEL

- Emission Permit Certificate

- Types, calorific values, fuel analysis (sulphur, nitrogen, ash, humidity, etc), fuel feeding rates (kg/hour), daily, monthly, annual and hourly consumption amounts of the fuels used in the facility.

- Distance of the facility to the closest settlement area, facility permit granted according to the Regulation on Non-Hygienic Facilities, settlement plan around the facility, if deemed necessary by the Ministry.

- Features of the existent emission and wastewater treatment facilities and treatment productivity of each of them in percentages.

- Flue gas debit, height of the stack (actual height of the stack and the height adjusted in Annex – 6 of the Regulation on the Protection of Air Quality shall be stated separately), flue gas outlet rate, flue gas temperature, diameter of the stack.

- Control and acceptance procedures applied before the generator delivers the waste oil, and when the waste oil comes in the facility. Laboratory analysis measurement devices used for this purpose. One copy of the license certificates and driver training certificates, if the facility has licensed waste transportation vehicles.

- Name, title, address, telephone and fax numbers of the personnel responsible for waste management in the facility.

- Information on the capacity and properties of waste oil tanks, waste preparation process, waste feeding systems and waste feeding points.

- Addresses of the facilities or companies selling waste oil, categories and amounts of waste oils, a copy of the agreement – if any - signed with the said facility or company on waste supply, and information on the supply of waste oil on a continuous basis.

- Measurement and controls to be carried out in the facility as per the Regulation on the Protection of Air Quality and the frequency of use of the related parameters.

- Information on contingency measures to be taken in the facility, names, liabilities and tasks of the personnel in charge, a copy of the contingency plan.

- Trial burn plan

- Other information and documentation required by the Ministry.

# ANNEX – 7

INFORMATION AND DOCUMENTATION FOR THE PRE- LICENSING APPLICATION FOR THE WASTE OIL RECOVERY FACILITIES

1- Application Form

2- General Information on the Facility

a) About the Facility:

- Commercial Title

- Address (Quarter, Street, No, District, Province)

- Telephone number

- Fax number

- E-mail address

b) About the owner/shareholders of the facility:

- Name, surname

- Address (Quarter, Street, No, District, Province)

- Telephone number

- Fax number

- E-mail address

c) About the operator of the facility:

- Name, surname

- Address (Quarter, Street, No, District, Province)

- Telephone number

- Fax number

- E-mail address

d) About the person/institution prepared the application:

- Name, surname (or title)

- Address (Quarter, Street, No, District, Province)

- Telephone number

- Fax number

- E-mail address

e) Other information:

- Possible date of commissioning

- Number and duties of the personnel to be employed in the facility

- Working hours of the facility (daily, monthly, annual)

- Vehicle and Machinery Park

- Social facilities (refectory, dormitory, changing rooms, toilet, wash-basin, bath – shower, infirmary, etc)

3- Information and Documentation on the Location of the Facility

- Topographical map of 1/25.000 scale plotting the location of the facility and 10 km of its periphery.

- Cadastral and land use maps plotting the location of the facility and its periphery and master plans.

- Ground and surface water resources under protection, locations where flood and landslide may occur.

4- Information on Operation

- For the facilities that are not subject to Environmental Impact Assessment, technical reports are required that are issued by the General Directorate of TÜPRAŞ and the relevant department of a university showing that the technology used in the waste oil recovery facility is in compliance with the waste oil types and products generated in the facility.

- Surface area of the facility

Indoors:		m2

Outdoors: 		m2

Total: 			m2

- Capacity of the facility

Installed capacity: 			ton/year

Actual capacity: 			ton/year

- Generation flow chart and technology

All the processes starting from the acceptance of wastes, recycling process should be explained in details. Treatment facility should be explained in details. Necessary charts, formulas and drawings shall be enclosed.

- Yield of waste oil recovery

- Companies supplying waste oil

- Names, amounts (ton/year) and storage methods of the chemical substances used in the waste processing

- Capacities of raw material tanks and product storage tanks and the safety measures to be taken

- Products generated following the recovery process, information on labeling and packaging of the products

- Types, components and amounts of un-recovered wastes and the disposal methods

5- Environmental Measures

(This information shall be supplied by the facilities that are not subject to the Regulation on Environmental Impact Assessment)

1) Water pollution

- Resources of utility water and process water in the facility

- well water

- tap water

- other

- Pollutants in the process water and measures to be taken

- Discharge points of utility water and process water

- Measures to be taken for the collection of storm water

2) Air pollution

- Fuel types and amounts to be used in the facility

- Units that may cause air pollution in the facility, their capacities and the number of the stacks in each of the units.

- Sources of dust and measures to be taken.

3) Noise pollution

- Sources of noise

- Measures to be taken

4) Soil pollution

- Measures to be taken so as to prevent soil pollution.

5) Smell pollution

- Measures to be taken so as to prevent smell pollution

6) Safety measures to be taken in the facility

- Fire

- Labor safety

- First aid

- Other

Date, Name – Surname and Signature of

Applicant / Authority of the Company

Note: All the documents included in the application file shall be signed and sealed.

# ANNEX – 8

INFORMATION AND DOCUMENTATION REQUIRED FOR LICENSING FOR WASTE OIL RECOVERY FACILITIES

1- Pre-license certificate

2- Conformity certificate certifying that the facility is constructed according to its project and specifications to prepared by the institutions responsible for the preparation of the technical report stated in Article 24. (Article 25)

3- Analysis and categories of the waste oils accepted to the facility.

4- Companies or facilities supplying waste oils, their addresses, telephone and fax numbers and responsible personnel.

5- Permit to be issued by the General Directorate of Petroleum Affairs, the Ministry of Energy and Natural Resources that allows the remarketing of the recovered base oil or other petroleum products (Article 27)

6- Standards, commercial names, generation amounts (ton/year) of the recovered products

7- Address, telephone and fax numbers of the companies purchasing the recovered products, responsible personnel of such companies, invoices, dispatch notes and weighing scale receipt of the sales.

8- Emission permit certificate, discharge permit certificate

9- Copies of the transportation licenses issued for the vehicles transporting the waste oils to the facility and from the facility for disposal after the related processes, national waste transportation forms, dispatch notes and copies of the invoices.

10- Types, properties and amounts of the process wastes (hazardous, non-hazardous, inert) generated by the facility and related disposal methods

11- Other documents:

- Tax office and tax number

- Work permit

- Copy of the Trade Registry Gazette

- Circulars of Signature

- Capacity Report

- Industry Certificate of Registration

- Operation Certificate (issued by the Ministry of Labor and Social Security)