DAMS AND HYDROELECTRIC POWER PLANTS  IN TURKEY (HEPPSs)

Main activities in dam construction accelerated after 1954 with the establishment of the DSI (General Directorate of State Hydraulic Works), subsequent legislation and establishment of regional administrations continued to spur dam development in the second half of the 20th Century. The environmental concerns are the one of the reasons for slowing the progress in dam construction activities in the country.

The first dam built during the republic era is the Cubuk-I Dam the main purpose of which is to meet the domestic water requirement of the city of Ankara. No serious activities in dam construction were observed until the end of Second World War except for a few small dams built for irrigation purposes. The largest multi-purposes dam constructed in Turkey is Atatürk Dam. Comparing with the reservoir capacity, Atatürk Dam is 8600 fold larger than Çubuk-I Dam.

According to the standards of ICOLD (International Committee on Large Dams), the dam is classified as a "large dam", if its height from foundation is more than 15 m, or its reservoir volume is equal or more than 3 hm3". The number of constructed large dams in Turkey is 673. The total reservoir capacity of 260 large dams is about 140 km3

DEVELOPMENT OF DAMS AS OF 2008

| DAM TYPE | IN OPERATION | UNDER CONSTRUCTION OR IN PROGRAM |
| --- | --- | --- |
|  | TOTAL | TOTAL |
| DAM | 673 | 146 |
| (LARGE-SCALE WATER PROJECTS) | 260 | 63 |
| (SMALL-SCALE WATER PROJECTS) | 413 | 83 |
| SMALL DAMS | 657 | 44 |

Dams in Turkey can be classified as follows according to crest types:

- Rock or earth-filled types: 650 dams

- Concrete gravity types: 8 dams

- Arch types: 6 dams

- Composite (Concrete Faced Rock – Fill Dam – CFRD or RCC) types: 9 dams

Owing to considerable variation observed in the run-off in terms of seasons, years and regions, it is absolutely necessary to have water storage on the rivers in Turkey. This ensures access to water when it is necessary. Construction of the dams in Turkey is not only for irrigation and hydropower production, but also for the long term domestic water supply. Consequently, Turkey has prioritized the construction of water storage facilities.

RESETTLEMENT POLICY AND PRACTICES

The resettlement of families that are adversely affected by infrastructure projects is regulated by the Resettlement Law in Turkey, which provides for state-assisted resettlement in both rural and urban areas. Resettlement action plans are prepared according to international standards, with the goal of minimizing the negative effects of resettlement and ensuring the maintenance of the current living standard and rehabilitating the income of the people living in the project area.While expropriation compensation payments are granted to all individuals properties, government assistance in resettlement is given to households rather than individuals. Families engaged in agriculture are resettled in rural areas, while families not engaged in agriculture are resettled in towns and cities.

ATATÜRK DAM

HYDROELECTRIC POTENTIAL

Currently, Turkey has 172 hydroelectric power plants in operation with total installed capacity of 13.700 MW generating an average of 48.000 GWh/year, which is 35% of the economically viable hydroelectric potential. 148 hydroelectric power plants are under construction 8.600 MW of installed capacity to generate average annual 20.000 GWh representing 14% of the economically viable potential. In the future, 1.418 more hydroelectric power plants will be constructed in order to make use of additional 22.700 MW installed capacity. As a result of these works, a total of 1.738 hydroelectric power plants with 45.000 MW will tame rivers to harness the economically viable hydropower of Turkey.

Annual energy consumption per capita in Turkey has reached 2.900 kWh which is above world average of 2.500 kWh. The average energy consumption for the developed countries is 8.900 kWh, but it varies from 12.322 kWh in the USA to 827 kWh in China. Annual increase in energy consumption is 8-10% in Turkey except for the recession years.

Total energy generation in Turkey in the 1950s was 800 GWh, this figure has increased by about 256 times, reaching 191.555 GWh/year today. As of 2008, the current installed capacity is 42.359 MW, which could generate an average of 246.974 GWh/year. Capacity utilization has been 87% in thermal plants and 70% in hydroelectric power plants. 19% of energy generation depends on hydroelectric power and the remaining 81% on thermal power. A special emphasis has recently been placed on alternative energy sources such as wind and geothermal power. The share of geothermal and wind power in total energy generation has reached 2%. There have been some steps taken towards introducing the use of nuclear power as well.

Turkey's theoretical hydroelectric potential is 1% of that of the World and 16% of Europe. The gross theoretical viable hydroelectric potential in Turkey is 433 billion kWh and the technically viable potential is 216 billion kWh. The economically viable potential, however, is 140 billion kWh

Status of economically viable potential of HEPPs

| STATUS OF ECONOMICALLY VIABLE POTENTIAL | NUMBER OF HYDRO-ELECTRIC POWER PLANTS | TOTAL INSTALLED CAPACITY (MW) | AVERAGE ANNUAL GENERATION (GWH/YEAR) | RATIO (%) |
| --- | --- | --- | --- | --- |
| In Operation | 172 | 13,700 | 48,000 | 35 |
| Under Construction | 148 | 8,600 | 20,000 | 14 |
| In Program | 1,418 | 22,700 | 72,000 | 51 |
| Total Potential | 1,738 | 45,000 | 140,000 | 100 |

DAMS AND HYDROPOWER STATIONS IN OPERATION IN TURKEY (CAPACITIES LARGER THAN 100 MW)

| No | Dam & Generating Facility | Construction | Location | Embank-ment Volume (1,000 m 3) | Crest Level (m) | Height | Normal Reservoir Volume (hm 3) | Lake Area (km 2) | Energy Benefit |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Starting Year | Completion Year | River | Province |  |  | From Foundation (m) | From River Bed (m) | Normal Water Level (m) |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  | Capacity (MW) | Annual Generation (GWh) |
| 1 | ATATÜRK | 1983 | 1992 | Fırat | Şanlıurfa | 84,500 | 549.00 | 169.00 | 166.00 | 542.00 | 48,700 | 817.00 | 2,400 | 8,900 |
| 2 | KARAKAYA | 1976 | 1987 | Fırat | Diyarbakır | 2,000 | 698.00 | 173.00 | 158.00 | 693.00 | 9,580 | 268.00 | 1,800 | 7,354 |
| 3 | KEBAN | 1965 | 1975 | Fırat | Elazığ | 15,585 | 848.00 | 207.00 | 163.00 | 845.00 | 31,000 | 675.00 | 1,330 | 6,000 |
| 4 | ALTINKAYA | 1980 | 1988 | Kızılırmak | Samsun | 16,000 | 195.00 | 195.00 | 140.00 | 190.00 | 5,763 | 118.31 | 700 | 1,632 |
| 5 | BİRECİK (2) | 1993 | 2000 | Fırat | Ş.Urfa | 9,209 | 389.00 | 63.50 | 53.50 | 385.00 | 1,220 | 56.25 | 672 | 2,518 |
| 6 | OYMAPINAR | 1977 | 1984 | Manavgat | Antalya | 676 | 185.00 | 185.00 | 157.00 | 184.00 | 300 | 4.70 | 540 | 1,620 |
| 7 | BERKE (2) | 1991 | 2001 | Ceyhan | K.Maraş | 735 | 346.00 | 201.00 | 186.00 | 345.00 | 427 | 7.80 | 510 | 1,672 |
| 8 | HASAN UĞURLU | 1971 | 1981 | Yeşilırmak | Samsun | 9,223 | 195.00 | 175.00 | 135.00 | 190.00 | 1,074 | 22.66 | 500 | 1,217 |
| 9 | SIR (2) | 1987 | 1991 | Ceyhan | K.Maraş | 494 | 443.00 | 116.00 | 106.00 | 440.00 | 1,120 | 47.50 | 284 | 725 |
| 10 | GÖKÇEKAYA | 1967 | 1972 | Sakarya | Eskişehir | 650 | 392.00 | 158.00 | 115.00 | 388.00 | 910 | 20.00 | 278 | 562 |
| 11 | BATMAN | 1986 | 1998 | Batman | Batman | 5,400 | 668.50 | 85.50 | 71.50 | 665.00 | 1,175 | 49.25 | 198 | 483 |
| 12 | KARKAMIŞ | 1996 | 1999 | Fırat | Maraş | 1,537 | 346.00 | 40.00 | 22.50 | 340.00 | 157 | 28 | 180 | 652 |
| 13 | ÖZLÜCE | 1985 | 1998 | Peri | Bingöl | 14,000 | 1,144.00 | 144.00 | 124.00 | 1140.00 | 1,075 | 25.80 | 170 | 413 |
| 14 | ÇATALAN | 1982 | 1996 | Seyhan | Adana | 17,000 | 130.00 | 82.00 | 70.00 | 125.00 | 2,126 | 81.86 | 169 | 596 |
| 15 | SARIYAR (2) | 1950 | 1956 | Sakarya | Ankara | 568 | 480.00 | 108.00 | 90.00 | 475.00 | 1,900 | 83.83 | 160 | 400 |
| 16 | GEZENDE | 1979 | 1990 | Ermenek | İçel | 83 | 335.00 | 75.00 | 71.00 | 333.00 | 92 | 3.97 | 159 | 528 |
| 17 | ASLANTAŞ | 1975 | 1984 | Ceyhan | Adana | 8,493 | 160.00 | 95.00 | 78.00 | 146.00 | 1,150 | 49.00 | 138 | 569 |
| 18 | HİRFANLI | 1953 | 1959 | Kızılırmak | Kırşehir | 2,000 | 860.00 | 83.00 | 78.00 | 851.00 | 5,980 | 263.00 | 128 | 400 |
| 19 | MENZELET | 1980 | 1989 | Ceyhan | K.Maraş | 8,700 | 614.50 | 156.50 | 136.50 | 609.40 | 1,950 | 42.00 | 124 | 515 |
| 20 | KILIÇKAYA | 1980 | 1989 | Kelkit | Sivas | 6,900 | 855.00 | 134.00 | 103.00 | 850.00 | 1,400 | 64.42 | 124 | 332 |
| 21 | DİCLE | 1986 | 1997 | Dicle | Diyarbakır | 2,180 | 718.00 | 87.50 | 75.00 | 715.50 | 595 | 24.00 | 110 | 298 |

ENERGY PROJECT WITH IN THE CONTENT OF LAW 4628

For the realization of the hydroelectric energy projects, DSI requested from the Grand National Assembly of Turkey to prepare a law so that private sector can invest for the realization of project for shorter period than DSİ. This law is called "4628 Electricity Market Law" and its licensing regulation which comply with the free market economy. This agreement also defines the procedures and principles of water uses together with the other user's rights.

"4628 Electricity Market Law" has become effective in 2001. The first article of this law defines the objective, which is to supply electricity to the users in adequate quantity, in high quality, continuously and compatible with the environment by providing financially strong stable and transparent and competitive electricity market complying with the special law rules and independently controlled.

Within the framework of the "4628 Electricity Market Law", regulation related with the procedures and principles of signing Water Use Right Agreement for production activities in electricity market was prepared in 2003, and private sector applications according to this regulation has started since then.

In total 1524 hydroelectric power projects with 22360 MW installed capacity has been implemented until January 22, 2009. However, 426 projects have been granted with licensing, and out of this number, construction of 135 projects has been started.

ALMUS

ALTINKAYA

YASSIÇAL

DOYRAN

HATİPLER

ASLANTAŞ

MARDİN

BAKLAN

KARAKAYA

SARIYAR

KOZVİRAN

YENİCE

YEŞİLÇAY

| DAMS & HEPPs CONSTRUCTED AS LARGE-SCALE WATER PROJECTS BY DSI |
| --- |
| 1. Çubuk I 2. Gölbaşı 3. Gebere 4. Elmalı II (*) 5. Sarıyar (*) 6. Seyhan 7. Ayrancı 8. Kemer 9. Hirfanlı 10. Demirköprü 11. Sille 12. May 13. Mamasın 14. Apa 15. Seyitler 16. Çubuk II 17. Selevir 18. Bayındır 19. Cip 20. Kızılsu 21. Almus 22. Kesikköprü 23. Gülüç (*) 24. Tatların 25. Buldan 26. Altınapa 27. Kurtboğazı 28. Akkaya 29. Gümüşler 30. Onaç I 31. Altınyazı 32. Akköy 33. Sarımsaklı 34. Sürgü 35. Musaözü 36. Gölköy 37. Çaygören 38. Damsa 39. Kesiksuyu 40. Alakır 41. Kadıköy 42. Kozan 43. Kartalkaya 44. Porsuk 45. Enne 46. Ömerli 47. Devegeçidi 48. Hasanlar 49. Gökçekaya 50. Atıkhisar 51. Yalvaç 52. Karamanlı 53. Karaçomak 54. K. Kalecik 55. Tahtaköprü | 56. Medik 57. Çoğun 58. Keban 59. Korkuteli 60. Dodurga 61. Çorum 62. Yapıaltın 63. Maksutlu 64. Kaymaz 65. Afşar 66. Ataköy 67. Balçova 68. Süloğlu 69. Asartepe 70. Karaidemir 71. Hasanuğurlu 72. Bozkır 73. Sevişler 74. Güzelhisar 75. Suatuğurlu 76. Kunduzlar 77. Uluköy 78. Alibey 79. Doğancı 80. Kültepe 81. Demirtaş 82. Gökçeada 83. Arpaçay 84. Boztepe 85. Söğüt 86. Topçam 87. Aslantaş 88. Berdan 89. Alaca 90. Belpınar 91. Oymapınar 92. Uluborlu 93. Hasanağa 94. Çamlıdere 95. İvriz 96. Yedikır 97. Germeçtepe 98. Kalecik 99. Kozağacı 100. Sarıbeyler 101. Tayfur 102. Kayalıköy 103. Kozlu 104. Ağcaşar 105. Kayaboğazı 106. Çatören 107. B. Çekmece 108. Karakaya 109. Manavgat (*) 110. Çakmak | 111. Gödet 112. Güldürecek 113. Gölova 114. Ketsel 115. Kovalı 116. Hancağız 117. Zernek 118. Altınkaya 119. Geyik 120. Gökçe 121. Darlık (*) 122. Tercan 123. Altınhisar 124. Kapulukaya 125. Sarayözü 126. Karacaören I 127. Yarseli 128. Hacıhıdır 129. Ürkmez 130. Uzunlu 131. Mumcular 132. Polat 133. Kılıçkaya 134. Menzelet 135. Adıgüzel 136. İkizcetepeler 137. Yahyasaray 138. Gezende 139. Çavdarhisar 140. Derbent 141. Yapraklı 142. Koçköprü 143. Patnos 144. Dumluca 145. Gayt 146. Mursal 147. Çamköy 148. Göksu 149. Sarımehmet 150. Sır (*) 151. Atatürk 152. Büyükorhan 153. Eğrekkaya 154. Sultansuyu 155. Murtaza 156. Beyler 157. Gazibey 158. Örenler 159. Küre-Çatak 160. Gelingüllü 161. Seferihisar 162. Sultanköy 163. Kızılcapınar 164. Karacaören II (*) 165. Nergizlik | 166. Kuzgun 167. Demirdöven 168. Kırklareli 169. Yaylakavak 170. Tahtalı 171. Gönen 172. Bayramiç 173. Çavdır 174. Çatalan 175. Sazlıdere 176. Alaçatı (*) 177. Madra 178. Çat 179. Kralkızı 180. Armağan 181. Dicle 182. Çamlıgöze 183. Yenihayat 184. Karaova 185. Erzincan 186. Bademl 187. Özlüce 188. Yayladağ 189. Sıddıklı 190. Bakacak 191. Batman 192. Çamgazi 193. Akyar 194. Yenice 195. Karkamış 196. Kirazdere (*) 197. Çayboğazı 198. Sorgun 199. Birecik (*) 200. Kızıldamlar 201. Gökpınar 202. Palandöken 203. Berke (*) 204. Derinöz 205. Kürtün 206. İmranlı 207. Küçükler 208. Ayhanlar 209. Dört Eylül 210. Bahçelik 211. Suğla Dep 212. Koruluk |

| HYDROELECTRIC POWER PLANT PROJECTS TO BE HELD FOR TENDER |
| --- |
|  | NAME | PROJECT OWNER | POWER (MW) | AVERAGE (GWh) | ACCREDITED (GWh) | CITY | DISTRICT | REGION | AIM | TENDERS | DATE (FROM-TO) |
| 1 | KIZILÇAĞIL REG. VE HES | EİE | 1,33 | 5,85 | 0,78 | DENİZLİ | KIZILÇAĞIL DERE | AYDIN | ELECTRICITY | BOYUT GRUP ENERJİ VE İNŞAAT SAN. TİC. LTD. ŞTİ. | 07.05.2009 | 06.06.2009 |
| 2 | KESKİN BARAJI VE HES | EİE | 164,00 | 740,00 | 359,00 | SİİRT | BOTAN ÇAYI | VAN | ELECTRICITY | BİTLİS ENERJİ ÜRETİM İÇ VE DIŞ TİCARET A. Ş. | 25.05.2009 | 24.06.2009 |
| 3 | KÖPRÜLER-GEM | DSİ | 2,16 | 14 | 9 | VAN | GÜRPINAR | VAN | ELECTRICITY | ON THE AGENDA |
| 4 | GÖKÇEKISIK HES | DSİ | 2,00 | 9 | 2 | ESKİŞEHİR | MERKEZ | ESKİŞEHİR | ELECTRICITY | ON THE AGENDA |
| 5 | BAŞKALE | EİE | 5,70 | 19 | 15 | HAKKARİ | DİCLE | VAN | ELECTRICITY | ON THE AGENDA |
| 6 | DOĞUBEYAZIT | DSİ | 4,50 | 30 | 27 | AĞRI | D.BEYAZIT | ERZURUM | ELECTRICITY | ON THE AGENDA |
| 7 | YAHYAKÖY REG. VE HES | DSİ | 3,75 | 11,49 | 0,95 | BALIKESİR | MERKEZ | BALIKESİR | ELECTRICITY+IRRIGATION | ON THE AGENDA |
| 8 | CÜRÜMÖREN | DSİ | 6,00 | 13 | 11 | KASTAMONU | DEVREKANİ | KASTAMONU | ELECTRICITY | ON THE AGENDA |
| 9 | FINDIKLI BARAJI VE HES | EİE | 30,00 | 87 | 78 | ERZİNCAN |  | ERZURUM | ELECTRICITY | ON THE AGENDA |
| 10 | ESENYAMAÇ | EİE | 9,00 | 25,00 | 14,00 | HAKKARİ | MERKEZ | VAN | ELECTRICITY | ON THE AGENDA |
| 11 | AŞIKLAR | EİE | 1,24 | 7,22 | 3,42 | RİZE |  | TRABZON | ELECTRICITY | ON THE AGENDA |
| 12 | KAYNAR | EİE | 1,29 | 6,00 | 1,00 | TOKAT |  | SAMSUN | ELECTRICITY | ON THE AGENDA |
| 13 | KAYADİBİ REG. VE HES | EİE | 1,06 | 5,58 | 0,81 | SAMSUN | YEŞİLDERE | SAMSUN | ELECTRICITY | ON THE AGENDA |
| 14 | BEKÇAN REG. VE HES | EİE | 0,81 | 4,04 | 0,99 | AFYON | SÖĞÜTÖZÜ DERESİ | ISPARTA | ELECTRICITY | ON THE AGENDA |
| 15 | SORGUN REG. VE HES | EİE | 1,16 | 5,46 | 1,00 | BİLECİK | SORGUN DERE | ESKİŞEHİR | ELECTRICITY | ON THE AGENDA |
| 16 | YASSITAŞ REG. VE HES | EİE | 2,65 | 9,03 | 0,22 | MERSİN | YASSITAŞ DERE | ADANA | ELECTRICITY | ON THE AGENDA |
| 17 | AYDIN REG. VE HES | EİE | 1,50 | 5,15 | 1,13 | ARTVİN | AYDIN DERE | ARTVİN | ELECTRICITY | ON THE AGENDA |
| 18 | ALATA REG. VE HES | EİE | 0,97 | 3,87 | 0,49 | ANTALYA | KAYADİBİ DERE | ANTALYA | ELECTRICITY | ON THE AGENDA |
| 19 | SİSNE REG. VE HES | EİE | 1,04 | 4,20 | 0,52 | K.MARAŞ |  | K.MARAŞ | ELECTRICITY | ON THE AGENDA |
| 20 | TAPSUR REG. VE HES | EİE | 1,65 | 6,28 | 1,47 | ERZURUM | TAPSUR DERE | ERZURUM | ELECTRICITY | ON THE AGENDA |
| 21 | ŞEHİR REG. VE HES | EİE | 1,24 | 6,14 | 4,10 | ERZURUM | ŞEHİR DERE | ERZURUM | ELECTRICITY | ON THE AGENDA |
| 22 | TÜNKEŞ REG. VE HES | EİE | 1,06 | 4,38 | 1,96 | ERZURUM | TÜNKEŞ DERE | ERZURUM | ELECTRICITY | ON THE AGENDA |
| 23 | KARASU BARAJI VE HES | EİE | 22,00 | 57,00 | 33,00 | HAKKARİ | KARASU DERE | VAN | ELECTRICITY | ON THE AGENDA |
| Source: DSI; MAY 2009 |  |  |  |  |  |  |  |  |  |
| EIE: General Directorate of Electrical Power Resources Survey and Development Administrative (www.eie.gov.tr) |
| DSİ: General Directorate of State Hydraulic Works (www.dsi.gov.tr) |

TURKEY

LAND AND WATER RESOURCES

Turkey possesses a number of different characteristics in terms of its geographical location. The total length of its land borders and coastline is 10,765 km, 2,949 km of which are the land borders while 7,816 km are the coastline. Turkey has borders with Greece and Bulgaria to the west, with Georgia, Armenia, Azerbaijan and Iran to the east and with Iraq and Syria to the south.

The border with Bulgaria (269 km) extends from the mouth of the Rezve Stream in the Black Sea to the north west of Edirne. The border with Greece (203 km) extends along the Meriç River, passing around Edirne and Karaağaç and emptying into the Aegean Sea to the west of Enez. The total length of the border with Georgia (276 km), the border with Armenia (328 km) and Azerbaijan border (18 km) is 622 km, beginning from Sarp Village and extending along the Arpaçay and Aras rivers. The border with Iran (560 km) follows the summits of high mountains with extending up to the Kelsim Breach at the beginning of the Iraq border. The border with Iraq (384 km) ends at the point where the Tigris and Habur rivers meet after passing through high and mountainous territory in the vicinity of Hakkari. The border with Syria (911 km) runs immediately south of the Baghdad Railway, reaching the Mediterranean in Güvercinkaya.

The average altitude (1,132 m) of Turkey is higher than that (1,050 m) of Asia and three and a half times higher than that (330 m) of Europe. The elevation of Turkey increases from the west to the east. The altitude of Ulus, the centre of Ankara, is 875 m. The altitude of plains in the eastern region rises to 2,000 m.

Turkey’s surface area is 780,000 km2, namely 78 million hectares (Mha). Excluding the total area of reservoirs and lakes, Turkey’s land area is 769,600 km2. Excluding mountainous areas which cover a little more than half of the total land area, Turkey has plains, plateaux, steep and rugged land, and flat hills. Plains of different altitudes covered with alluvium amount to 19 Mha. Plateaux cover 8 Mha. The total area of plains and plateaux is equal to 27 Mha, which is 30% of Turkey’s land. Rugged terrains with flat, wide hills amount to 10 Mha. Since agricultural operations are often relatively easy in these type of rugged terrains, 10 Mha might be added to 27 Mha as flat lands. Therefore, Turkey has about 37 Mha of flat lands. However, Turkey’s total agricultural area is about 28 Mha. The General Population Census of 2000 indicates that Turkey has a population of 67.8 million in a total of 81 provinces. The average population density is 88 persons per square kilometer.

RIVERS AND LAKES

Turkey has about 120 natural lakes, including small lakes in the mountains. The largest and deepest lake is Lake Van with a surface area of 3,712 km2 and an altitude of 1,646 m from sea level. The second largest lake is Lake Tuz in central Anatolia. Being relatively shallow, this lake is at an altitude of 925 m from sea level and has a surface area of 1,500 km 2. There are four main regions where lakes are intensively dispersed: The “Lakes District” (Eğirdir, Burdur, Beyşehir, and Acıgöl Lakes), Southern Marmara (Sapanca, İznik, Ulubat, and Kuş Lakes), Lake Van and its environs, and Lake Tuz and its environs. Although some of the lakes are only a few meters in depth, some of them are of a depth of more than 30 meters. The depth of Lake Van is more than 100 m.

Turkey has 555 large dam reservoirs. The names and surface areas (km2) of the large ones are Atatürk (817), Keban (675), Karakaya (268), Hirfanlı (263), Altınkaya (118), Kurtboğazı (6).

Turkey is rich in terms of streams and rivers. Many rivers rise and empty into seas within Turkey’s borders. Rivers can be classified in relation to the sea into which they empty. The rivers emptying into the Black Sea are the Sakarya, Filyos, Kızılırmak, Yeşilırmak, and Çoruh. The rivers emptying into Mediterranean Sea are the Asi, Seyhan, Ceyhan, Tarsus, and Dalaman. The rivers emptying into the Aegean Sea are the Büyük Menderes, Küçük Menderes, Gediz, and Meriç. The rivers empting into the Sea of Marmara are the Susurluk/Simav, Biga, and Gönen. The Euphrates and Tigris rivers empty into the Gulf of Basra, while the Aras and Kura rivers empty into the Caspian Sea. As far as the lengths of the some major rivers are concerned, the Kızılırmak is 1,355 km, Yeşilırmak is 519 km, Ceyhan is 509 km, Büyük Menderes is 307 km, Susurluk is 321 km, the Tigris is 523 km, the Euphrates River up to the Syrian border is 1,263 km, and the Aras River up to the Armenia border is 548 km.

CLIMATE

Turkey has a semi-arid climate with some extremities in temperature. Turkey is surrounded by seas on three sides and high mountains stretching along the Black Sea coast in the north and along the Mediterranean Sea coast in the south. Distance from sea and fluctuations in altitude result in climatic variance within short distances. Temperature, precipitation and winds vary, based on climatic features. The difference in the north to the south latitude (6 0) also plays a role in this temperature change. The southern coastal fringes enjoy the Mediterranean climate featuring hot, dry summers and mild, rainy winters. The northern coastal fringes are of the Black Sea climate, which is mild and rainy in almost all seasons. Surrounded by high mountains, Central Anatolia features a steppe climate with little precipitation and daily and yearly temperature values differing significantly. Winters are long and cold in Central and Eastern Anatolia, while mild and short in coastal regions.

PRECIPITATION VARIES BY FAR WITH RESPECT TO THE REGION AND PERIOD

Especially the mountainous coastal regions receive abundant precipitations (1,000–2,500 mm/year). Inner parts away from coastal fringes receive relatively less precipitation. Precipitation is 500–1,000 mm/year in the Marmara and Aegean regions and in the plateaux of East Anatolia. Most parts of Central Anatolia and Southeastern Anatolia have precipitation only 350–500 mm annually, whereas the environs of Lake Tuz receive the lowest precipitation level (250–300 mm/year).

Snow falls in almost every region of Turkey, but the number of days on which it snows and the durations of snow cover vary considerably with regard to the regions. It snows less than one day a year in the Mediterranean Region while more than 40 days in Eastern Anatolia on average. The duration of snow cover is less than one day in the Mediterranean and Aegean coastal fringes, 10–20 days in the Marmara and Black Sea coastal areas, 20–40 days in Central Anatolia, and 120 days in the Erzurum and Kars provinces in Eastern Anatolia. Throughout the four seasons, higher parts of the mountains retain snow, which melts slowly, feeding rivers and ground waters.

On account of its geographical features, Turkey has four distinctive seasons. Variation in altitude up to 5,000 m causes different climatic conditions in the same season.

LAND RESOURCES

Turkey ’s total land area is 78 Mha. Almost one third of this, 28 Mha, can be classified as cultivable land. Recent studies indicate that an area of about 8.5 million ha is economically irrigable under the available technology. Until now, an area of about 2.8 million ha has been equipped with irrigation infrastructures by DSİ.

WATER RESOURCES

Geographically, there is a large variation in annual precipitation, evaporation and surface run-off parameters, in Turkey. Precipitation is not evenly distributed in time and space throughout the country. There are 25 hydrological basins in Turkey. The rivers often have irregular regimes.

Considering the average surface water run-off which is 186 billion m3/year with the surface run-off of 7 billion m3/year coming from neighboring countries, the total surface run-off within the country reaches to the amount of 193 billion m3/year. On the other hand, the average amount of ground-water leakage is 41 billion m3/year. However, not all the renewable water resources can be utilized because of economic and technical reasons. Exploitable portions of surface run-off including inflow from bordering countries, and groundwater are 98 and 14 billion m3/year, respectively. Thus, the total of economically exploitable water resources potential amount to 112 billion m3/year.

DISTRIBUTION OF PRECIPITATION

The 25 hydrological basins in Turkey have a total surface water run-off of 193 billion m3/year. 31% of the potential is constituted by the Euphrates (Fırat) and the Tigris (Dicle) Rivers both of which have their sources in the eastern part of the country.

# Footnotes

DSİ IS A PRIMARY EXECUTIVE AGENCY RESPONSIBLE FOR ELIMINATION OF ADVERSE EFFECTS OF TURKEY’S SURFACE AND GROUND WATER AND PUTTING THEM IN PUBLIC UTULIZATION IN VARIOUS WAYS SUCH AS HYDROPOWER, IRRIGATION, DOMESTIC AND INDUSTRIAL USE

# Text boxes

HYROELECTRIC POWER PLANTS IN TURKEY